## Slide 1
Multi-Branch Network Automation
ASSIGNMENT
Mohamed Yasser Khalifa
TELECOM ENGINEER

## Slide 2
Table of Contents
MOHAMED YASSER KHALIFA
Problem
3
Network Architecture
4
Addressing
5
Automation Archeticture
6
Monitoring and Failover Logic
7
Mock Simulation
8

## Slide 3
Applies initial configurations to all routers and switches
1
Monitors the connectivity between branches
2
Automatically updates configurations if a link goes down
3
Problem
MOHAMED YASSER KHALIFA
3
Design a resilient, multi-branch architecture (HQ, Giza, Alexandria) with automated provisioning and self-healing.
You must design the IP addressing plan, network topology, and create a Python script that:

## Slide 4
Network Topology
MOHAMED YASSER KHALIFA
4

## Slide 5
WAN | 10.0.xy.0/30 | x--> WAN, y--> Link | 10.0.11.1
LAN | 10.x.y.0/24 | x--> branch, y--> VLAN | 10.1.10.0
Router to Switch | 10.x.0.0/30 | x--> branch | 10.1.0.1
loopback (management) | 10.x.x.x 10.xx.xx.xx | x--> branch | 10.1.1.1 10.11.11.11
Addressing & Routing
MOHAMED YASSER KHALIFA
5
STATIC ROUTING WAS SELECTED FOR THIS DESIGN

## Slide 6
Automation Archeticture
MOHAMED YASSER KHALIFA
6
  Day 0 Configuration
  Device Data (IP, Hostnames, DHCP Pools, ...)
    config.json
  NetworkConfigurator class — pushes initial configuration to all devices
    configure.py
  NetworkMonitor class — monitors WAN links and handles failover/failback
    monitor.py
  Orchestrator — loads config, calls configure, starts monitoring loop
    main.py

## Slide 7
Ping Results | Current Role | Action
Success | Primary active | Do nothing — link healthy
Success | Backup active | Failback — restore primary route
Fail | Primary active | Failover — push backup route
Fail | Backup active | Do nothing — backup already active
Monitoring and Failover Logic
MOHAMED YASSER KHALIFA
7
The NetworkMonitor class runs a continuous loop, checking WAN link health every 10 seconds using system ping commands via Python's subprocess module.

## Slide 8
Testing & Simulation (Mock Mode)
MOHAMED YASSER KHALIFA
7
A simulation layer that replaces real network communication with predefined Cisco IOS responses, allowing the system to be tested and validated without requiring physical devices.
Link Failure Triggering:
Simulates a WAN outage by automatically forcing ping failures after a defined time, allowing the failover mechanism to be tested and validated.

## Slide 9
The End
THANK YOU FOR LISTENING
Mohamed Yasser Khalifa